## Slide 1
ECE4700J Summer 2026
Computer Architecture
Design Review II:
Implementation and Testbench Progress
Yanze Yu, Haotian Xu, Zixiang Wang, Xu Zhang
Global College, Shanghai Jiao Tong University
June 21, 2026
1
Notes: \

## Slide 2
Agenda
2
Current Progress
Second-Period Module Overview
Module Implementation Updates
Testbench Coverage and Results
Figure / Evidence Placeholders
Timeline: DR I to DR III
Challenges and Next Steps
Notes: 单击此处添加文本

## Slide 3
Team Leader: Current Progress
3
Task | Implemented | Test Result | Next Step
D-cache eviction outputs | Yes | System TB blocked by interface | Fix dcache_if.cpu modport
LRU replacement | Yes | basic_lru test PASS | Clean full verbose TB
Next-line prefetcher | Yes | 7-group TB PASS | Integrate with cache path
Victim cache | Yes | TB written; compile blocked | Run conflict-miss regression
Second-period docs | Partial | README covers modules | Add performance evidence
Notes: 单击此处添加文本

## Slide 4
4
Second-Period Module Overview
Module | Main Ports / Direction | Role in Design | Current Status
simple_dcache update | evict_valid/addr/data: output | Expose displaced line to victim cache | Implemented; interface fix needed
basic_lru | update_en/set/way: input; victim_way: output | Replacement policy for VC / future set-assoc | Basic TB PASS
prefetcher | upstream: dram; downstream: cache_mem | One-line next-line buffer | Dedicated TB PASS
victim_cache | upstream: dram; downstream: cache_mem; evict_* in | Catch conflict misses from L1 | Source + TB written
testbench_prefetcher | BFM request/response | Verify cold, hit, write invalidation, in-flight | PASS
tb_victim_cache | CPU-L1-VC-DRAM topology | Verify conflict miss and VC hit path | Compile blocked
Conflict miss | Read 0x00000100 | Same index, different tag | 
Notes: 单击此处添加文本

## Slide 5
Module: D-cache Update
5
What changed since DR I:
- simple_dcache now exposes evict_valid, evict_addr, evict_data
- Eviction fires when a valid L1 line is displaced on a refill
- Write miss path separated into refill and write-through stages
- This prepares the baseline cache for victim-cache integration
Testbench focus:
- Existing directed d-cache tests cover read miss, read hit, write hit, write miss, conflict miss
- Current blocker: Verilator reports cpu_if.ready/rdata are driven through an input-only modport
- Fixing the interface direction is the next priority
□ Figure placeholder: waveform / block diagram / terminal output
Notes: 单击此处添加文本

## Slide 6
Module: LRU Replacement
6
Implementation:
- Parameterized NUM_SETS x NUM_WAYS tracker
- age = 0 means most recently used
- largest age is selected as victim_way
- Used by victim_cache as one-set, four-way replacement
Testbench focus:
- testbench_lru.sv checks victim order after touches
- Local run passed: 3 -> 2 -> 1 -> 0 -> 3 victim sequence
- full LRU TB targets 4-way + 2-way golden-model testing
- Full TB currently needs variable/reference cleanup
□ Figure placeholder: waveform / block diagram / terminal output
Notes: 单击此处添加文本

## Slide 7
Module: Next-Line Prefetcher
7
Implementation:
- Interposes between L1 miss bus and DRAM
- Stores one prefetched block in a buffer
- Demand requests have priority over prefetches
- Writes invalidate matching prefetched lines
- Exposes issue/fill/hit counters
Testbench focus:
- Cold demand read launches next-line prefetch
- Prefetched read is faster and chains another prefetch
- Non-sequential miss replaces buffered line
- Write invalidates stale prefetched data
- In-flight next-line request is captured
□ Figure placeholder: waveform / block diagram / terminal output
Notes: 单击此处添加文本

## Slide 8
Module: Victim Cache
8
Implementation:
- Four-entry fully associative victim cache
- Placed between simple_dcache and dram_model
- Read hit returns block directly without DRAM access
- Read miss / writes forward downstream
- Absorbs L1 evictions through evict_* ports
Testbench focus:
- CPU-L1-VC-DRAM topology is written
- Intended flow: read A, read conflicting B, re-read A from VC, then L1 hit
- Also prints VC entries and eviction pulses
- Current compile is blocked by the d-cache modport issue
□ Figure placeholder: waveform / block diagram / terminal output
Notes: 单击此处添加文本

## Slide 9
9
Testbench: D-cache and Victim Cache
Test | Access Pattern | Expected Result | Status
D-cache read miss | Read cold block | Fetch block from DRAM | TB exists
D-cache read hit | Read same address again | Immediate cache data | TB exists
D-cache write hit | Write cached word | Update cache and memory | TB exists
D-cache write miss | Write uncached block | Write-allocate then write-through | TB exists
Victim conflict path | A, B same index, re-read A | VC hit, no DRAM | TB written
Current blocker | Compile L1 with CPU modport | ready/rdata driven legally | Needs fix
Figure note | □ Add waveform/terminal output | Show eviction pulse and VC hit | Placeholder
Notes: 单击此处添加文本

## Slide 10
10
Testbench: LRU Replacement
Test | Access Pattern | Expected Result | Status
Reset init | rst asserted | way age initializes by way index | Covered
Sequential touches | Touch 3,2,1,0 | Victim rotates 2,1,0,3 | PASS
Hold behavior | update_en = 0 | victim_way stays stable | In full TB
Multi-set independence | Update one set, read another | Other set unchanged | In full TB
2-way boundary | NUM_SETS=1, NUM_WAYS=2 | Correct victim toggle | In full TB
Pseudo-random | 100-step deterministic sequence | Match software model | In full TB
Current blocker | Compile full TB | All groups run | Needs ev/reference fix
Notes: 单击此处添加文本

## Slide 11
11
Testbench: Next-Line Prefetcher
Test | Access Pattern | Expected Result | Status
Cold read | Read ADDR_0 | Return DRAM data and issue ADDR_1 prefetch | PASS
Prefetch hit | Read ADDR_1 | Faster than cold miss; hit counter increments | PASS
Non-sequential | Read ADDR_4 | Replace old buffer with ADDR_5 | PASS
Write invalidate | Write buffered line | Buffered copy becomes invalid | PASS
Read after write | Read same block | Return written data via memory path | PASS
In-flight demand | Read next line while prefetch busy | Captured and served | PASS
Counters | End of test | 7 issues, 7 fills, 2 hits | PASS
Notes: 单击此处添加文本

## Slide 12
12
Figure / Evidence Placeholders
□ Figure placeholder: top-level module connection diagram
□ Figure placeholder: LRU terminal PASS output
□ Figure placeholder: prefetcher terminal PASS output
□ Figure placeholder: victim-cache waveform after modport fix
Notes: 单击此处添加文本

## Slide 13
Timeline: DR I to DR III
13
Phase | Start Date | End Date | Specific Arrangements | Status
Ongoing | 5/29/2026 | 7/1/2026 | Basic testing after each main commit and test modules during implementation | Active
DR I prep | 6/8/2026 | 6/10/2026 | Design Review I preparation | Done
Second period | 6/10/2026 | 6/22/2026 | 2-way set-associative, LRU/FIFO, basic prefetch, fully-associative victim cache | In Progress
DR II prep | 6/20/2026 | 6/22/2026 | Design Review II preparation | Current
Debug / measure | 6/23/2026 | 7/1/2026 | Stress testing, debugging, performance measurement | Next
MSHR start | 6/25/2026 | 7/1/2026 | Initial MSHR design and initial non-blocking cache | Next
DR III prep | 6/29/2026 | 7/1/2026 | Design Review III preparation | Next
Today
6/21
Notes: 单击此处添加文本

## Slide 14
Challenges & Next Steps
14
CHALLENGES
NEXT STEPS
Interface direction: simple_dcache drives ready/rdata through input-only cpu modport.
Full LRU TB: broad coverage, but current file needs variable/reference cleanup.
System evidence: victim-cache test cannot run until interface fix.
Figure evidence: insert screenshots/waveforms after passing regressions.
Fix dcache_if modport and rerun d-cache + victim-cache testbenches.
Keep prefetcher and basic_lru tests as smoke tests after each commit.
Add terminal screenshots/waveforms into the square placeholders.
Before DR III: stress testing, performance counters, and initial MSHR direction.
Notes: 单击此处添加文本